## Slide 1
.
Background
CONAC was proposed for SM drives with input voltage saturation
Stability and constraint satisfaction were ensured via Lyapuonv theory
As future work, the following subjects will be investigated
  The parameter dependencies of CONAC
  Real-time implementation to validate the effectiveness and feasibility
Numerical Validation
Contributions
Constraints formulation
Constrained optimization problem
Constraint 1: Weight boundedness (1 hidden layer)
Constraint 2: Input saturation
Adaptation law derivation
No prior system information is required
Adaptation laws are derived based on constrained optimization
Stability is guaranteed using Lyapunov theory, see Thm. 1 in Paper
Motivation 1:
Exact system knowledge is required, e.g., resistances and flux linkages
Motivation 2:
Input saturation by
voltage source inverter (VSI)
Lagrangian function
Gradient descent/ascent methods (dual problem)
Constrained Optimization-Based Neuro-Adaptive Control (CONAC) for Synchronous Machine Drives Under Voltage Constraints (ID: 1360)
Myeongseok Ryu*, Niklas Monzen**, Pascal Seitter**, Kyunghwan Choi* and Christoph M. Hackl**
(*) CCS Graduate School of Mobility, KAIST, Republic of Korea and (**) LMRES, Hochschule Műnchen, Germany
Conclusion
Nomenclature
Quadratic objective function of tracking error
Proposed Method (CONAC)
Fig 1. Current tracking results
Fig 2. Norm of control input (voltage)
Tracking Performance
Both controllers demonstrated satisfactory performance
Performance was improved in Episode 2, ≅ -84%
(C2) achieved slightly higher performance
  However, it neglected costs that come from saturation
Input Saturation
Input saturation of (C1) was suppressed
(C2) exceeded the input limit, ≅ +85%
(C1) CONAC with input constraint
(C2) CONAC without input constraint
Reference current
Table 1. Quantitative comparison of performances’ norm
SM drive modeling
Design current tracking controller
Utilize ANN to approximate unknown ideal input (Motivation 1)
Derive ANN weight adaptation law ensuring stability (weight and error boundedness) and preventing input saturation (Motivation 2)
Fig 3. Lagrange multipliers in logarithmic scale
Constraint Handling
Lagrange multipliers increase to adjust adaptation, see eq. (3)
Lagrange multipliers adjust adaption direction
Saturation (VSI)
Unknown terms
Control input (voltage)
State (current)
Controller design objectives
Resistances
Flux linkages
Nomenclature
Ideal unknown control input
Actual input (ANN output)
This work was supported in part by GIST-IREF from Gwangju Institute of Science and Technology (GIST), was supported in part by the National Research Foundation of Korea (NRF) grant funded by the Korea government (MSIT) (RS-2025-00554087)